## Slide 1: Condition Assessment of Stay Cables through Enhanced Time Series Classification Using a Deep Learning Approach ---- Project 3 of IPC-SHM 2020
The 1st International Project Competition for Structural Health Monitoring
IPC-SHM 2020
June 15 - September 30, 2020, Harbin, China
Zhiming Zhang*, Louisiana State University
Jin Yan, Iowa State University
Liangding Li, University of Central Florida
Hong Pan, North Dakota State University
Chuanzhi Dong, University of Central Florida
*Email: zzhan59@lsu.edu
08/31/2020

## Slide 2
Project 3 of IPC-SHM 2020: Goal & Tasks
Conclusions & Future Work
Methodology: TSC via Deep Learning with the LSTM-FCN Model
Experimental Case study: Results & Discussions
Outline
IPC-SHM 2020

## Slide 3
Project 3: Condition Assessment of Stay Cables
    Basic info:
      cable-stayed bridge
      168 stay cables (84 pairs)
      dataset:
        cable tension force
        load cell
        sampling frequency: 2 Hz
        14 cables: SJS08 to SJS14 and SJX08 to SJX14
        10 days: (2006-05-13 to 2006-05-19, 2007-12-14, 2009-05-05, and 2011-11-01)
    Goal: find the damaged cable
      data preprocessing
      feature extraction
      statistical model development

## Slide 4
Methodology
Time series classification
      wide applications in health care, financial analysis, etc.
      cable damage detection
        data X: segments of measure time series
          Scenario 1: cable force of a certain cable (SJS08)
          Scenario 2: cable force ratio of a certain cable pair (SJ08 = SJS08/SJX08)
        label Y: ID of cable or cable pair
          Scenario 1: e.g., SJS08
          Scenario 2: e.g., SJ08
cable i
data 1
data 2
data l
data n
label i
label i
label i
label i
X Y
TSC

## Slide 5
Methodology
Time series classification
cable i
data 1
data 2
data l
data n
label i
label i
label i
label i
cable j
data 1
data 2
data l
data n
label j
label j
label j
label j
cable k
data 1
data 2
data l
data n
label k
label k
label k
label k
intact condition
TSC model
cable j
data 1
data 2
data l
data n
label j
label j
label j
label j
cable i
data 1
data 2
data l
data n
label i
label i
label i
label i
cable i
data 1
data 2
data l
data n
label i
label i
label i
label i
cable j
data 1
data 2
data l
data n
label m
label p
label i
label k
test
test
intact condition
damaged condition
model training
model testing

## Slide 6
Methodology
LSTM-FCN model for TSC (Karim et al. 2017)
      reduced preprocessing compared with other deep learning models
      components
        input layer
        FCN module
          Conv layer
          ReLU activation function
          global average pooling
        LSTM module
          feature augmentation
          regularization
          dimension shuffle
            reduce overfitting
        feature concatenation
        softmax layer
dimension shuffle
LSTM
dropout
input (cable force/cable force ratio)
Conv1D
ReLU
Conv1D
ReLU
Conv1D
ReLU
global pooling
concatenate
softmax

## Slide 7
Experimental case study
    Project 3: condition assessment of stay cables
    Data preprocessing
      outlier
      sensor failure
    LSTM-FCN model Configuration & training
    Results and discussions
      Scenario 1 with cable force as input
      Scenario 2 with cable force ratio as input
      Decision making on the damaged cable
Data Preprocessing
LSTM-FCN
Scenario 1
Scenario 2

## Slide 8
Preprocessing: outlier
    outlier: extreme values
    remove outliers based on the range elsewhere
(b) SJX13 with outlier
(a) SJS13 with outlier
(c) SJS13 with outlier removed
(d) SJX13 with outlier removed

## Slide 9
Preprocessing: sensor failure
    SJS08
      periodicity pattern
        traffic loads
        environment
    Day 10 on SJX08 & SJX13
      notably small magnitude
      small fluctuation
      reversal or random drift
      sensor failure
cable force: SJS08 (a) to (j): day 1 to day 10
cable force: SJX08 (a) to (j): day 1 to day 10
cable force: SJX13 (a) to (j): day 1 to day 10

## Slide 10
Preprocessing: data segmentation and assignment
    data segmentation
      172800 = 108*1600
      referring to UCR datasets
      label each segment with the class ID
    training and testing data
      data prior to 2011
        50% for training
        50% for testing
      data in 2011
        test using the learned model
…
172800
1600*108
…
training
testing
data prior to 2011
data in 2011
LSTM-FCN model

## Slide 11
Investigated scenarios
    Scenario 1:
      input: cable force
      target: 14 cable labels
    Scenario 2:
      input: cable force ratio
      target: 7 cable pair labels
score on cable 1 (SJS08)
score on cable 2 (SJS09)
…
score on cable 14 (SJX14)
cable force
LSTM-FCN model
score on cable pair 1 (SJ08)
score on cable pair 2 (SJ09)
…
score on cable pair 7 (SJ14)
cable force ratio
LSTM-FCN model

## Slide 12
LSTM-FCN Model Configuration and Training
    Framework
      Keras library with the TensorFlow backend
    Parameters
      cell number of LSTM
      number of Conv layers in FCN
      kernel size of Conv layers
    Training settings
      2000 epochs
      initial batch size:128
      Adam optimizer
      adaptive learning rate
    Evaluation metric: accuracy
128*1 256*1 128*1
(kenrl size)
cell number: 8

## Slide 13
Results
    Classification accuracy
      pre-2011: data prior to the year of 2011
      overall-2011: all data in 2011
      SJS/SJX**: data in 2011 labeled with cable ID in Scenario 1
      SJ**: data in 2011 labeled with cable pair ID in Scenario 2
dataset | pre- 2011 | overall-2011 | SJS08 | SJS09 | SJS10 | SJS11 | SJS12 | SJS13 | SJS14
accuracy | 0.79 | 0.56 | 0.53 | 0.69 | 0.59 | 0.28 | 0.65 | 0.89 | 0.55
dataset | - | - | SJX08 | SJX09 | SJX10 | SJX11 | SJX12 | SJX13 | SJX14
accuracy | - | - | - | 0.83 | 0.25 | 0.60 | 0.61 | - | 0.60
dataset | pre- 2011 | overall-2011 | SJ08 | SJ09 | SJ10 | SJ11 | SJ12 | SJ13 | SJ14
accuracy | 0.96 | 0.75 | - | 0.94 | 0.95 | 0.02 | 0.94 | - | 0.91
Scenario 1
Scenario 2

## Slide 14
Results
    Decision making: combining the results of Scenarios 1 & 2
      Scenario 1: possible damage in cables SJS11 and SJX10
      Scenario 2: possible damage in cable pair SJ11
      the most probable cable with damage: SJS11
      consistent with results in [1]: SJ11
      improvement
[1] Li, S., Wei, S., Bao, Y. and Li, H. 2018, “Condition assessment of cables by pattern recognition of vehicle-induced cable tension ratio”, Engineering Structures 155, 1–15.
SJS
SJX
SJ

## Slide 15
Conclusions and future work
    This study proposes detecting cable damage from collected cable force data through time series classification (TSC) using the deep learning framework LSTM-FCN.
    Two scenarios are investigated with different input and class labels
    Combining the results of the two scenarios, the most probable damaged cable is detected, which is consistent with the results in the literature.
    This proposed method enables fast and convenient early detection and warning in real applications.
    More case studies will be conducted in the future work.

## Slide 16
Acknowledgment
    Our team would like to acknowledge the organizing committee of the 1st International Project Competition for structural health monitoring (IPC-SHM 2020) for sharing all the materials used in Project 3 for cable condition assessment
    We also would like to thank the committee for kindly replying to our inquiries every time. They did great job!